## Slide 1: Chapter 3: Transport Layer
UDP

## Slide 2: Transport layer functionality
7: Application
4: Transport
3: Network
2: Data link
1: Physical
7: Application
4: Transport
3: Network
2: Data link
1: Physical
7: Application
4: Transport
3: Network
2: Data link
1: Physical
Application services
Logical communications
Inter-process comm.
Segmentation and reassembly
Error checking
Multiplexing via sockets
Congestion control
Flow control
Reliability
In-order delivery
Notes: How can messages get out of order?: different paths, retransmissions

## Slide 3: Multiplexing and Demultiplexing
UDP
Packets demuxed by:
  Destination IP
  Destination port
Packets from (153.90.118.46,3541) and (128.111.52.235,5502) would go to the same socket
TCP
Packet demuxed by:
  Destination IP
  Destination port
  Source IP
  Source port
Packets from (153.90.118.46,3541) and (128.111.52.235,5502) would go different sockets
s = socket.socket(socket.AF_INET, socket.SOCK_DGRAM)
s.bind((‘127.0.0.1’, 5000))
s = socket.socket(socket.AF_INET, socket.SOCK_STREAM)
s.bind ((‘127.0.0.1’, 80))
s.listen(1)
conn, addr = s.accept()
http://en.wikipedia.org/wiki/ List_of_TCP_and_UDP_port_numbers
UDP sockets identified
(dst_IP:dst_port) tuple
TCP sockets identified
(src_IP:src_port, dst_IP:dst_port) four-tuple
Notes: Why not all the ports below 1024 are used?
Why have this reserved range?
Port scanning
Why have the different demultiplexing mechanisms in UDP and TCP? (hint: DNS runs on UDP, web servers on TCP)
Support for threading on TCP (or different connection for each request in non-persistent HTTP) – different service per client
UDP: same service per client with lower state

## Slide 5: UDP Packet structure
Header information:
  Source and destination ports for demux
  Checksum for error detection
  Packet length in bytes (headers and data)
src_port
dst_port
length
checksum
Application
data
(message)
UDP Packet Format
32-bits
Data in 16-bit words
Wrap around: add overflow
Form one’s complement
Error checking
Recompute at receiver
Add result to passed checksum
Error if not all zeros
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
+ 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
= 1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
+ 1
= 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
Why use packet headers, as opposed to JSON?
Where are source and destination IP addresses?
Why not send fixed length packets?
Notes: Why headers?
  Easier to process
  Don’t need whole packet before forwarding processing
What happens when error in checksum?

## Slide 6: UDP Checksum Exercise
Consider the following bits
src_port
dst_port
length
checksum
Application
data
(message)
UDP Packet Format
32-bits
0001001110001000
0001011101110000
0000000000010000
1010010001111101
0001010110010101
0001001011000110
0001000011010100
1000100101100101
0000010010101100
0110100100111010
Identify the fields of a UDP packet
Is the UDP packet correct?
In practice UDP checksum includes fields from IP header
0001001110001000 0001011101110000
0000000000010000 1010010001111101
0001010110010101 0001001011000110
0001000011010100 1000100101100101
0000010010101100 0110100100111010
Notes: Sum: 0101 1011 1000 0011
Complement: 1010010001111100
Sum: 1110110110011100
One’s complement: 0001001001100011
No guarantee error checking at routers
Could get errors while packets are sitting in send buffers

## Slide 7: UDP header and pseudo IP header
In practice UDP checksum includes routing information
RFC 768 defines UDP checksum calculation
Includes fields in the pseudo IPv4 (or IPv6) header available to in the UDP socket
RFC 768: “This information gives protection against misrouted datagrams.”

## Slide 8: Which transport protocol where?
In order delivery
Large pages
Large file sizes
High rate of transfer
Fixed data rate
Email size > UDP packet size
Fixed data rate
No connection delay
No connection delay

## Slide 9: User Datagram Prot. (UDP)
“No frills,” “bare bones” Internet transport protocol
Based on “best effort” network model
  UDP segments can be lost
  Or delivered out-of-order
Connection-less
No support for:
  Flow control
  Congestion control
  In-order delivery
  Reliability
Advantages of UDP:
Immediate transmission
  No connection establishment
  No delayed transmission
Fixed/immediate sending rate
  No ramp up
Lower memory requirements
  No connection state
Small packet overhead
  8B for UDP vs 20B for TCP
Disadvantages:
Controversial in streaming applications
Blocked by many firewalls
Notes: Mainly used for control traffic – where service the same for all clients